## Slide 1: Indian Particle Accelerator Conference InPAC-2015
W. Beeckman, M. Cavellier, S. Antoine, P. Bocher, O. Cosson, F. Forest,
N. Huttin, P. Jehanno, P. Jivkov, C. Kellener, A. Kreiss, J.L. Lancelot, M.J. Leray, X. Milpied, R. Riedinger, O. Tasset,
SIGMAPHI, F-56000 Vannes, FRANCE
A.S. Fomichev, L.V. Grigorenko, V.I. Kazacha, S.A. Krupko, S.V. Stepantsov, G.M. Ter-Akopian
Flerov Laboratory of Nuclear Reactions, JINR, RU-141980 Dubna, Russia
Status of the Acculinna-2 RIB Fragment Separator
Dr Matthieu CAVELLIER
SIGMAPHI - France
December 22, 2015 - B2 - Session IV- Paper No 370

## Slide 2: The Acculinna-2 Fragment separator In-flight RIB separator
U400
F1 Target
Primary
beam
Selected
RIB(s)
Acculinna-2
Selector
F5
Target
adds 1p / 0n
Unstable
nucleus
Decay
0° dipole
Detectors
measurement
Decay nuclei
(Neutrons)
(Protons)
RIBs
Projectile
fragments
 direction
 energy
Projectile
fragmentation
18Ne
17F
16O
15N
20Ne
P~17%
18Ne
18Ne
(p,d)
17Ne*
15O
1p
1p
17Ne*
Decay
Acculinna-2
Selector
20Ne7+
54 AMeV
20Ne7+
fragmentation
Solid Be
18Ne
+ others

## Slide 3: Acculinna-2 in perspective

## Slide 4: Layout

## Slide 5: From contract to installation October 2011 to December 2013

## Slide 6: Scope of Sigmaphi’s responsibility
Being in control of these 4 techniques gives full freedom for an optimized design leading to an energetically efficient and cost effective facility
Optics check
All magnets
All power supplies
All vacuum
Installation
Alignment
Shaping chambers to reduce bores
Trading gradient for length
Standardizing magnets … within limits
Trading current for turns
Trading copper for voltage
Using standard power supplies
…
Optimization candidates
Power consumption
Cost of
Standardization
design
material
fabrication
Figures of merit
But above all
preserve functional specs

## Slide 7: Shaping vacuum chambers to reduce bore
Good field region much closer to pole edge.
Great care in design

## Slide 8: Shaping vacuum chambers to reduce bore
Q12
Q13
Q14

## Slide 9: Trading Power supply VS coil
INTEGRATED gradient i.e. gradient times length is important to the beam
Gradient can be traded for length if
Optics remains OK
Space between elements permits
Gradient - Length
Current
For static magnets, voltage is decided by Ohm’s law
and Pouillet’s law states
Voltage
Good choice
(U,I) in the range of an existing PS
Aim at low Power
Larger coil
Aim at standardization for coils
Copper = Voltage &
cross-section Power
n & I = Cheap coil & power supply
n & I = Big coil & power supply

## Slide 10: Standardization
Standardization groups objects with “similar” properties
Advantages
Huge reduction in cost for design, tooling and fabrication
Exchangeability and servicing
Drawbacks
Slightly sub-optimal design
Higher material costs
PARTIAL standardization might already help a lot keeping most of the advantages while taming drawbacks
Example of Secondary quadrupoles
1 lamination, 1 length, 1 coil
QM11 (1 item) = Q1
QM21 (1 item) = Q2
QM22 (7 items) = Q4,Q5,Q7,Q8,Q11,Q12,Q14
QM31 (1 item) = Q3
QM32 (4 items) = Q6,Q9,Q10,Q13
1 lamination, 2 lengths, 2 coils
1 lamination, 2 lengths, 2 coils
3 lamination, 5 coils, 5 designs instead of 14

## Slide 11: Optimization reduces operation costs … for years !
Grouping
Reducing bore with tailored chambers
More copper to reduce power supply and PS standardization
41% savings in power consumption

## Slide 12: Installation from start to end January 2014 – March 2015
Room 1

## Slide 13: Installation from start to end January 2014 – March 2015
Before January 2014
January 2014
September 2014
September 2014

## Slide 14: Installation of power supplies and vacuum

## Slide 15: Floor reinforcement in Room 2
Room 2

## Slide 16: Floor reinforcement in Room 2
Room 2
Resistance limited to 1 ton/m²
~11 tons
~9.1 tons

## Slide 17: Floor reinforcement in Room 2
Febr 18 2015
March 17 2015
March 6 2015
March 2 2015
Building structure pillars

## Slide 18: Alignment
Chart: 
Leica laser tracker AT401
Alignment accuracy within ± 0.1 mm

## Slide 19: Conclusion
ACCULINNA-2 is fully installed and commissioned. Running started a few weeks ago.
Last week: Beam hit target F2 with 100% transmission.
It is on time and on budget.
A global contract for all hardware has opened the possibility for thorough optimization and drastic improvements of the long term operation costs.
A wonderful human experience!
Near future:
  Zero-angle dipole spectrometer designed, production starts soon, delivery : June 2016
  Cryogenic tritium target in 2017

## Slide 20: Thank you for your attention धन्यवाद Спасибо

## Slide 21: Back up slides

## Slide 22: Zero angle spectrometer
Neutron detector
Stylbene crystals scintillator array
distance to F5 > 3m
TOF accuracy 1%
Protons
Br = 0.4 ~ 1.0 Tm
Cone 0 ~ 14°
Br=0.4
Br=1.0
±14°
Heavy decay products
Br = 1.1 ~ 1.7 Tm
Cone 0 ~ 6°
Br=1.1
Br=1.7
±6°
Position sensitive hodoscope (multi-wire proportional chambers)
Si DE-E annular
telescopes near the target

## Slide 23: Zero angle spectrometer
Yoke 12.2 tons
Coils 3 tons
3.3m
1.6m
0.3m

## Slide 24: Costs
Costs coincides vey well with early predictions
The separator itself (same cost for RIPS at RIKEN)
All communications (electricity, water, vacuum)
Zero degree spectrometer
Civil constructions (new cabin, production target and radiation shell)
Beam diagnostics and vacuum control (Faraday cups, slits, profilometers, tof-detectors, valves etc)
RF kicker (in the plan for the next 7 years)
New tritium target (gas-vacuum system, safety surroundings etc)
Total for ALL planned equipment
In M$
5
0.1
0.3
0.25
0.15
1
1
7.8
Relatively low cost of our setup is explained by
existing infrastructure (cyclotron, experimental hall, communications etc);
simple and cost effective design (no SC elements, no high tech, optimized system)
A pigmy compared to FAIR (~1200 M€), FRIB (450 M$), BigRIPS or SPIRAL2
Known
Estim’d

## Slide 25: References
Acculinna webpage + list of publications
http://aculina.jinr.ru/acc-2.php
An extended study of the Acculinna2 configuration with LISE++
http://lise.nscl.msu.edu/9_4/acculinna2/9_4_acculinna2.pdf
Research program for the radioactive beams of the ACCULINNA-2 separator
http://aculina.jinr.ru/pdf/Research%20Program%20for%20the%20Radioactive%20Beams%20of%20the%20ACCULINNA-2%20Separator.pdf
The status of new fragment separator ACCULINNA-2 project and the first day experiments
http://aculina.jinr.ru/pdf/epjconf_inpc2013_11021.pdf